## Slide 1: Mass Spectrometry

## Slide 2: Mass spectrometry
technique for measuring the masses and relative abundances of components in a mixture
produces a mass spectrum
  Y-axis: Relative Abundance
  X-axis: Mass/Charge ratio

## Slide 3
Uses:
find masses of isotopes in a sample
determine structural components of molecules

## Slide 4
sample
A beam of electrons is used to ionize the atoms in the sample
Negatively-charged plates attract the ions.
A magnetic field is used to deflect the ions.
The ion is detected electrically when it reaches the end of the tube.

## Slide 5
Ionization
  electrons are knocked off of sample
  1+ ions are generated
  small proportion of 2+
Acceleration
  negatively-charged plates attract the ionized particles

## Slide 6
Deflection
  an applied magnetic field deflects (changes the path of) the charged particles
  degree of deflection - two factors:
    mass of particle: Lighter particles are deflected more
    charge of particle (don’t need to consider since most are 1+)

## Slide 7
Detection
  ion hits detection plate  generates a current
  current is translated into an electrical signal
  intensity of signal indicates relative abundance in the original sample
      more intense = more abundant
most abundant
Notes:   alter which ions reach the detector by varying the applied magnetic field

## Slide 8
example: sample of Cl2
Qualitative Interpretation
two distinct isotopes: Cl-35 and Cl-37
Cl-35 is more abundant

## Slide 9
Quantitative Interpretation
higher peak is assigned a relative abundance of 100
translate to percent abundances:
Cl-35:
100
Cl-37:
35
100
(100+35)
x 100%
= 74%
% abundance Cl-35:
35
(100+35)
x 100%
= 26%
% abundance Cl-37:
Now calculate weighted atomic mass of Chlorine!

## Slide 10
Alternative - Calculating relative atomic mass in one step:
Cl-35:
100
Cl-37:
35
(100 x 35) + (35 x 37)
(100 + 35)
= 35.52

## Slide 11: Good Animation
https://www.youtube.com/watch?v=tOGM2gOHKPc